## Slide 1: Module – 3 Data protection – raid (redundant array of independent disks)
Module 3: Data Protection - RAID
1
Notes: Module – 3
Data Protection – RAID

## Slide 2
Upon completion of this module, you should be able to:
  Describe RAID implementation methods
  Describe the three RAID techniques
  Describe commonly used RAID levels
  Describe the impact of RAID on performance
  Compare RAID levels based on their cost, performance, and protection
Module 3: Data Protection – RAID

## Slide 3: Module 3: Data Protection – RAID
During this lesson the following topics are covered:
  RAID Implementation methods
  RAID array components
  RAID techniques
Lesson 1: RAID Overview

## Slide 4: Why RAID?
Due to mechanical components in a disk drive it offers limited performance
An individual drive has a certain life expectancy and is measured in MTBF (mean time between failures):
  For example: If the MTBF of a drive is 750,000 hours, and there are 1000 drives in the array, then the MTBF of the array is 750 hours (750,000/1000)
RAID was introduced to mitigate these problems
It is a technique that combines multiple disk drives into a logical unit (RAID set) and provides protection, performance, or both.
RAID

## Slide 5: RAID Implementation Methods
Software RAID implementation
  Uses host-based software to provide RAID functionality
  Limitations
    Use host CPU cycles to perform RAID calculations, hence impact overall system performance
    Support limited RAID levels
    RAID software and OS can be upgraded only if they are compatible
Hardware RAID Implementation
  Uses a specialized hardware controller installed either on a host or on an array

## Slide 6: RAID Array Components
RAID Controller
Hard Disks
Logical Array
(RAID Sets)
RAID Array
Host

## Slide 7: RAID Techniques
Three key techniques used for RAID are:
  Striping
  Mirroring
  Parity

## Slide 8: RAID Technique – Striping
RAID
Controller
Host
Stripe
Strip

## Slide 9: RAID Technique – Mirroring
Host
Block 0
RAID
Controller
Block 0
Block 0

## Slide 10: RAID Technique – Parity
RAID
Controller
D1
D2
D3
D4
P
4
6
1
7
18
Host
Actual parity calculation is a bitwise XOR operation

## Slide 11: Data Recovery in Parity Technique
Host
4 + 6 + ? + 7 = 18
? = 18 – 4 – 6 – 7
? = 1
Regeneration of data when Drive D3 fails:
D1
D2
D3
D4
P
4
6
?
7
18
RAID
Controller

## Slide 12: Module 3: Data Protection – RAID
During this lesson the following topics are covered:
  Commonly used RAID levels
  RAID impacts on performance
  RAID comparison
  Hot spare
Lesson 2: RAID Levels

## Slide 13: RAID Levels
Commonly used RAID levels are:
  RAID 0 – Striped set with no fault tolerance
  RAID 1 – Disk mirroring
  RAID 1 + 0 – Nested RAID
  RAID 3 – Striped set with parallel access and dedicated parity disk
  RAID 5 – Striped set with independent disk access and a distributed parity
  RAID 6 – Striped set with independent disk access and dual distributed parity

## Slide 14: RAID 0
RAID Controller
C
B
A
Data from host
Data Disks
A1
A2
A3
A4
A5
B1
B2
B3
B4
B5
C1
C2
C3
C4
C5

## Slide 15: RAID 1
F
E
D
C
B
A
Data from host
Mirror Set
Mirror Set
A
A
D
D
B
B
E
E
C
C
F
F
RAID Controller

## Slide 16: Nested RAID – 1+0
C
B
A
Data from host
Mirror Set C
Mirror Set A
Mirror Set B
RAID Controller
A1
B1
C1
A1
B1
C1
A2
B2
C2
A2
B2
C2
A3
A3
B3
B3
C3
C3
Striping
Mirroring
Mirroring
Mirroring

## Slide 17: RAID 3
RAID Controller
C
B
A
Data from host
Data Disks
Dedicated Parity Disk
A1
A2
A3
A4
AP
B1
B2
B3
B4
BP
C1
C2
C3
C4
CP

## Slide 18: RAID 5
RAID Controller
C
B
A
Data from host
Distributed Parity
A1
A2
A3
A4
AP
B1
B2
B3
BP
B4
C1
C2
CP
C3
C4

## Slide 19: RAID 6
RAID Controller
C
B
A
Data from host
Dual Distributed Parity
A1
A2
A3
AP
AQ
B1
B2
BP
BQ
B3
C1
CP
CQ
C2
C3

## Slide 20: RAID Impacts on Performance
  In RAID 5, every write (update) to a disk manifests as four I/O operations (2 disk reads and 2 disk writes)
In RAID 6, every write (update) to a disk manifests as six I/O operations (3 disk reads and 3 disk writes)
In RAID 1, every write manifests as two I/O operations (2 disk writes)
Cp new
RAID Controller
+
-
=
C4 old
Cp old
C4 new
1
2
3
4
A1
A2
A3
A4
AP
B1
B2
B3
BP
B4
C1
C2
CP
C3
C4

## Slide 21: RAID Penalty
Every write operation that translates into more I/O overhead for the disks

## Slide 22: RAID Penalty Calculation Example
Total IOPS at peak workload is 1200
Read/Write ratio 2:1
Calculate disk load at peak activity for:
  RAID 1/0
  RAID 5

## Slide 23: Solution: RAID Penalty
For RAID 1/0, the disk load (read + write)
= (1200 x 2/3) + (1200 x (1/3) x 2)
= 800 + 800
= 1600 IOPS
For RAID 5, the disk load (read + write)
= (1200 x 2/3) + (1200 x (1/3) x 4)
= 800 + 1600
= 2400 IOPS

## Slide 24: RAID Comparison
RAID level | Min disks | Available storage capacity (%) | Read performance | Write performance | Write penalty | Protection
1 | 2 | 50 | Better than single disk | Slower than single disk, because every write must be committed to all disks | Moderate | Mirror
1+0 | 4 | 50 | Good | Good | Moderate | Mirror
3 | 3 | [(n-1)/n]*100 | Fair for random reads and good for sequential reads | Poor to fair for small random writes fair for large, sequential writes | High | Parity (Supports single disk failure)
5 | 3 | [(n-1)/n]*100 | Good for random and sequential reads | Fair for random and sequential writes | High | Parity (Supports single disk failure)
6 | 4 | [(n-2)/n]*100 | Good for random and sequential reads | Poor to fair for random and sequential writes | Very High | Parity (Supports two disk failures)
where n = number of disks

## Slide 25: Suitable RAID Levels for Different Applications
RAID 1+0
  Suitable for applications with small, random, and write intensive (writes typically greater than 30%) I/O profile
  Example: OLTP, RDBMS – Temp space
RAID 3
  Large, sequential read and write
  Example: data backup and multimedia streaming
RAID 5 and 6
  Small, random workload (writes typically less than 30%)
  Example: email, RDBMS – Data entry

## Slide 26: Hot Spare
Hot spare
Failed disk
Replace failed disk
RAID Controller

## Slide 27: Module 3: Summary
Key points covered in this module:
RAID implementation methods and techniques
Common RAID levels
RAID write penalty
Compare RAID levels based on their cost and performance

## Slide 28: Exercise 1: RAID
A company is planning to reconfigure storage for their accounting application for high availability
  Current configuration and challenges
    Application performs 15% random writes and 85% random reads
    Currently deployed with five disk RAID 0 configuration
    Each disk has an advertised formatted capacity of 200 GB
    Total size of accounting application’s data is 730 GB which is unlikely to change over 6 months
    Approaching end of financial year, buying even one disk is not possible
Task
  Recommend a RAID level that the company can use to restructure their environment fulfilling their needs
  Justify your choice based on cost, performance, and availability

## Slide 29: Exercise 2: RAID
A company (same as discussed in exercise 1) is now planning to reconfigure storage for their database application for HA
  Current configuration and challenges
    The application performs 40% writes and 60% reads
    Currently deployed on six disk RAID 0 configuration with advertised capacity of each disk being 200 GB
    Size of the database is 900 GB and amount of data is likely to change by 30% over the next 6 months
    It is a new financial year and the company has an increased budget
Task
  Recommend a suitable RAID level to fulfill company’s needs
  Estimate the cost of the new solution (200GB disk costs $1000)
  Justify your choice based on cost, performance, and availability