## Slide 1: Module – 5 Fibre channel storage area network (FC SAN)
Module 5: Fibre Channel Storage Area Network
1
Notes: Module – 5
Fibre Channel Storage Area Network (FC SAN)

## Slide 2
Upon completion of this module, you should be able to:
  Describe FC SAN and its components
  Describe FC architecture
  Describe FC SAN topologies and zoning
  Describe virtualization in SAN environment
Module 5: Fibre Channel Storage Area Network (FC SAN)

## Slide 3: Module 5: Fibre Channel Storage Area Network (FC SAN)
During this lesson the following topics are covered:
  Evolution of FC SAN
  Components of FC SAN
  FC interconnectivity options
  FC port types
Lesson 1: Overview of FC SAN

## Slide 4: Business Needs and Technology Challenges
An effective information management solution must provide:
  Just-in-time information to business users
  Flexible and resilient storage infrastructure
Information management challenges in direct-attached storage (DAS) environment:
  Explosive growth of information storage that remains isolated and underutilized
  Proliferation of new servers and applications
  Complexity in sharing storage resources across multiple servers
  High cost of managing information
Storage area network (SAN) addresses these challenges

## Slide 5: What is a SAN?
Centralizes storage and management
Enables sharing of storage resources across multiple servers at block level
Meets increasing storage demands efficiently with better economies of scale
Common SAN deployments are:
  Fibre Channel (FC) SAN: uses FC protocol for communication
  IP SAN: uses IP-based protocols for communication
It is a high-speed, dedicated network of servers and shared storage devices.
SAN

## Slide 6: Understanding Fibre Channel
High-speed network technology
  Latest FC implementation supports speed up to 16 Gb/s
Highly scalable
  Theoretically, accommodate approximately 15 million devices
Clients
Storage Arrays
Application Servers
IP
Network
FC SAN

## Slide 7: Components of FC SAN
Node (server and storage) ports
Cables
Connectors
Interconnecting devices such as FC switches and hubs
SAN management software

## Slide 8: Node Ports
Provide physical interface for communicating with other nodes
Exist on
  Host bus adapter (HBA) in server
  Front-end adapters in storage
Full-duplex data transmission mode
Each port has a transmit (Tx) link and a receive (Rx) link
Link
Port 0
Rx
Tx
Node
Port 0
Port 1
Port n

## Slide 9: Cables
SAN implementation uses
  Copper cables for short distance
  Optical fiber cables for long distance
Two types of optical cables: single-mode and multimode
Single-mode | Multimode
Carries single beam of light | Can carry multiple beams of light simultaneously
Distance up to 10km | Used for short distance (Modal dispersion weakens signal strength after certain distance )
Multimode Fiber
Single-mode Fiber

## Slide 10: Connectors
Attached at the end of a cable
Enable swift connection and disconnection of the cable to and from a port
Commonly used connectors for fiber optic cables are:
  Standard Connector (SC)
    Duplex connectors
  Lucent Connector (LC)
    Duplex connectors
  Straight Tip (ST)
    Patch panel connectors
    Simplex connectors
Straight Tip Connector
Lucent Connector
Standard Connector

## Slide 11: Interconnecting Devices
Commonly used interconnecting devices in FC SAN are:
  Hubs, switches, and directors
Hubs provide limited connectivity and scalability
Switches and directors are intelligent devices
  Switches are available with fixed port count or modular design
  Directors are always modular, and its port count can be increased by inserting additional 'line cards' or 'blades'
  High-end switches and directors contain redundant components

## Slide 12: SAN Management Software
A suite of tools used in a SAN to manage interfaces between host and storage arrays
Provides integrated management of SAN environment
Enables web-based management using GUI or CLI

## Slide 13: FC Interconnectivity Options
Point-to-Point
Fibre Channel Arbitrated Loop (FC-AL)
Fibre Channel Switched Fabric (FC-SW)

## Slide 14: Point-to-Point Connectivity
Enables direct connection between nodes
Offers limited connectivity and scalability
Used in DAS environment
Servers
Storage Array
Server
Server

## Slide 15: FC-AL Connectivity
Arbitrated loop
Provides shared loop to attached nodes
  Nodes must arbitrate to gain control
Implemented using ring or star topology
Limitations of FC-AL
  Only one device can perform I/O operation at a time
  Supports up to 126 nodes
  Addition or removal of a node causes momentary pause in loop traffic
Servers
Storage Array
Server
FC Hub

## Slide 16: FC-SW Connectivity
Switched fabric
Creates a logical space (called fabric) in which all nodes communicate with one another using switches
  Interswitch links (ISLs) enable switches to be connected together
Provides dedicated path between nodes
Addition/removal of node does not affect traffic of other nodes
Servers
Storage Array
Server
FC Switch
FC Switch
Interswitch Links

## Slide 17: Port Types in Switched Fabric
Server
N-Port
FC Switch
F-Port
FC Switch
Storage Array
N-Port
F-Port
E-Port
E-Port
Storage Array
N-Port
F-Port
ISL

## Slide 18: Module 5: Fibre Channel Storage Area Network (FC SAN)
During this lesson the following topics are covered:
  FC protocol stack
  FC addressing
  WWN addressing
  Structure and organization of FC data
  Fabric services
  Fabric login types
Lesson 2: Fibre Channel (FC) Architecture

## Slide 19: FC Architecture Overview
Provides benefits of both channel and network technologies
  Provides high performance with low protocol overheads
  Provides high scalability with long distance capability
Implements SCSI over FC network
  Transports SCSI data through FC network
Storage devices, attached to SAN, appear as local storage devices to host operating system

## Slide 20: Fibre Channel Protocol Stack
FC Layer | Function | Features Specified by FC Layer
FC-4 | Mapping interface | Mapping upper layer protocol (e.g. SCSI) to lower FC layers
FC-3 | Common services | Not implemented
FC-2 | Routing, flow control | Frame structure, FC addressing, flow control
FC-1 | Encode/decode | 8b/10b or 64b/66b encoding, bit and frame synchronization
FC-0 | Physical layer | Media, cables, connector
1 Gb/s
2 Gb/s
4 Gb/s
16 Gb/s
FC-4
FC-2
FC-1
FC-0
Upper Layer Protocol
Example: SCSI, HIPPI, ESCON, ATM, IP
Framing/Flow Control
Encode/Decode
8 Gb/s
Upper Layer Protocol Mapping

## Slide 21: FC Addressing in Switched Fabric
FC Address is assigned to nodes during fabric login
  Used for communication between nodes within FC SAN
Address format
Domain ID is a unique number provided to each switch in the fabric
  239 addresses are available for domain ID
Maximum possible number of node ports in a switched fabric:
  239 domains X 256 areas X 256 ports = 15,663,104

## Slide 22: World Wide Name (WWN)
Unique 64 bit identifier
Static to node ports on an FC network
  Similar to MAC address of NIC
  WWNN and WWPN are used to uniquely identify nodes and ports respectively
World Wide Name - Array
5
0101
0
0000
0
0000
6
0110
0
0000
1
0001
6
0110
0
0000
0
0000
0
0000
6
0110
0
0000
0
0000
1
0001
B
1011
2
0010
Company ID
24 bits
Port
Model Seed
32 bits
World Wide Name - HBA
1
0
0
0
0
0
0
0
c
9
2
0
d
c
4
0
Reserved
12 bits
Company ID
24 bits
Company Specific
24 bits
Format
Type
Format
Type

## Slide 23: Structure and Organization of FC Data
FC data is organized as Exchange, Sequence, and Frame
FC Data Structure | Description
Exchange | Enables two N_Ports to identify and manage a set of information units Information unit: upper layer protocol-specific information that is sent to another port to perform certain operation Each information unit maps to a sequence Includes one or more sequences
Sequence | Contiguous set of frames that correspond to an information unit
Frame | Fundamental unit of data transfer Each frame consists of five parts: SOF, frame header, data field, CRC, and EOF
SOF
4 Bytes
Data Field
0 - 2112 Bytes
CRC
4 Bytes
EOF
4 Bytes
Frame Header
24 Bytes
FC Frame

## Slide 24: Fabric Services
FC switches provide fabric services as defined in FC standards
Fabric Services | Description
Fabric Login Server | Used during the initial part of the node’s fabric login process Located at pre-defined address of FFFFFE
Name Server | Responsible for name registration and management of node ports Located at pre-defined address FFFFFC
Fabric Controller | Responsible for managing and distributing Registered State Change Notifications (RSCNs) to attached node ports Responsible for distributing SW-RSCNs to every other switch SW-RSCNs keep the name server up-to-date on all switches Located at pre-defined address FFFFFD
Management Server | Enables FC SAN management using fabric management software Located at pre-defined address FFFFFA

## Slide 25: Login Types in Switched Fabric
Fabric login (FLOGI)
  Occurs between an N_Port and an F_Port
  Node sends a FLOGI frame with WWN to Fabric Login Server on switch
  Node obtains FC address from switch
  Immediately after FLOGI, N_Port registers with Name Server on switch, indicating its WWN, port type, assigned FC address, etc.
  N_Port queries name server about all other logged in ports
Port login (PLOGI)
  Occurs between two N_Ports to establish a session
  Exchange service parameters relevant to the session
Process login (PRLI)
  Occurs between two N_Ports to exchange ULP related parameters

## Slide 26: Module 5: Fibre Channel Storage Area Network (FC SAN)
During this lesson the following topics are covered:
  Mesh and core-edge topologies
  Benefits of zoning
  Types of zoning
Lesson 3: FC SAN Topologies and Zoning

## Slide 27: Mesh Topology
Full mesh
  Each switch is connected to every other switch
  Maximum of one ISL or hop is required for host-to-storage traffic
  Host and storage can be connected to any switch
Partial mesh
  Not all the switches are connected to every other switch
FC Switches
Storage Array
Server
Full Mesh
FC Switches
Storage Array
Server
Partial Mesh

## Slide 28: Core-edge Topology
Consists of edge and core switch tiers
Network traffic traverses core tier or terminate at core tier
Storage is usually connected to the core tier
Benefits
  High availability
  Medium scalability
  Medium to maximum connectivity
FC Switch
FC Switch
FC Switch
Storage Array
FC Director
Server
Edge Tier
Core Tier
FC Switch
FC Switch
FC Switch
Storage Array
FC Director
Server
FC Director
Core Tier
Edge Tier

## Slide 29: Zoning
Zone set comprises zones
Each zone comprises zone members (HBA and array ports)
Benefits
  Restricts RSCN traffic
  Provides access control
It is an FC switch function that enables node ports within the fabric to be logically segmented into groups, and communicate with each other within the group.
Zoning
Storage Array
Servers
Array port
HBA Port
FC SAN
Server
Zone 1
Zone 2

## Slide 30: Types of Zoning
WWN Zoning
  Uses World Wide Names to define zones
  Zone members are the unique WWN addresses of the HBA and its targets (storage devices)
  Allows nodes to be moved to another switch port in the fabric and maintain connectivity to its zone partners without having to modify the zone configuration

## Slide 31: Types of Zoning
Port 1
Port 5
WWN 10:00:00:00:C9:20:DC:40
WWN 10:00:00:00:C9:20:DC:56
WWN 10:00:00:00:C9:20:DC:82
WWN 50:06:04:82:E8:91:2B:9E
Zone 1 (WWN Zone) = 10:00:00:00:C9:20:DC:82 ; 50:06:04:82:E8:91:2B:9E
Servers
Storage Array
FC Switch
Switch Domain ID = 15
Zone 1
Port 12
Port 9

## Slide 32: Types of Zoning
Port Zoning
  Uses the physical address of switch ports to define zones
  Access to node is determined by the physical switch port to which a node is connected
  Zone members are the port identifier (switch domain ID and port number) to which HBA and its targets (storage devices) are connected

## Slide 33: Types of Zoning
Zone 2
Port 1
Port 5
WWN 10:00:00:00:C9:20:DC:40
WWN 10:00:00:00:C9:20:DC:56
WWN 10:00:00:00:C9:20:DC:82
WWN 50:06:04:82:E8:91:2B:9E
Zone 2 (Port Zone) = 15,5 ; 15,12
Servers
Storage Array
FC Switch
Switch Domain ID = 15
Port 12
Port 9

## Slide 34: Types of Zoning
Mixed Zoning
  Combines the qualities of both WWN zoning and port zoning
  Using mixed zoning enables a specific node port to be tied to the WWN of another node

## Slide 35: Types of Zoning
Zone 3
Port 1
Port 5
WWN 10:00:00:00:C9:20:DC:40
WWN 10:00:00:00:C9:20:DC:56
WWN 10:00:00:00:C9:20:DC:82
WWN 50:06:04:82:E8:91:2B:9E
Zone 3 (Mixed Zone) = 10:00:00:00:C9:20:DC:56 ; 15,12
Servers
Storage Array
FC Switch
Switch Domain ID = 15
Port 12
Port 9

## Slide 36: Module 5: Fibre Channel Storage Area Network (FC SAN)
During this lesson the following topics are covered:
  Block-level storage virtualization
  Virtual SAN
Lesson 4: Virtualization in SAN

## Slide 37: Block-level Storage Virtualization
Provides a virtualization layer in SAN
Abstracts block storage devices and creates a storage pool by aggregating LUNs
Virtual volumes are created from storage pool and assigned to hosts
  Virtualization layer maps virtual volumes to LUNs
Benefits
  Online volume expansion
  Nondisruptive migration
Virtual Volume
Storage Array
Storage Array
Server
Virtualization
Appliance
Servers
LUN
LUN
LUN
LUN
FC SAN
Storage Pool

## Slide 38: Use Case: Block-level Storage Virtualization across Data Centers
Data Center 2
Data Center 1
Servers
Server
Server
Storage Arrays
Storage Arrays
Virtualization Layer
Virtualization Appliance
Virtual
Volumes
Servers
FC or IP
Virtual
Volumes
FC SAN
FC SAN

## Slide 39: Virtual SAN (VSAN)/Virtual Fabric
Each VSAN has its own fabric services (name server, zoning), configuration, and set of FC addresses
VSANs improve SAN security, scalability, availability, and manageability
It is a logical fabric on an FC SAN, enabling communication among a group of nodes, regardless of their physical location in the fabric.
VSAN
Storage Array
Storage Array
Servers
Servers
Server
Server
FC SAN
VSAN 20
VSAN 10

## Slide 40: Module 5: Fibre Channel Storage Area Network (FC SAN)
  EMC Connectrix
  EMC VPLEX
Concept in Practice:

## Slide 41: EMC Connectrix
Connectrix family includes networked storage connectivity products
  Offers high-speed FC connectivity, highly resilient switching technology, intelligent IP storage networking, and I/O consolidation with Fibre Channel over Ethernet
Connectrix family consist of enterprise directors, departmental switches, and multi-purpose switches

## Slide 42: EMC VPLEX
Provides solution for block-level storage virtualization and data mobility – both within and across data centers
Enables multiple hosts located across two locations to access a single copy of data
Provides capability to mirror a virtual volume – both within and across locations
  Allows hosts at different data centers to simultaneously access cache-coherent copies of the same virtual volume
VPLEX family consists of three products
  VPLEX Local
  VPLEX Metro
  VPLEX Geo

## Slide 43: Module 5: Summary
Key points covered in this module:
FC SAN components and connectivity options
FC protocol stack and addressing
Structure and organization of FC data
Fabric services
Fabric topologies
Types of zoning
Block-level storage virtualization and virtual SAN

## Slide 44: Exercise: FC SAN
Current situation
  An organization’s IT infrastructure consists of three storage arrays direct-attached to a heterogeneous mix of 45 servers
  Servers are dual-attached to the arrays to ensure high availability
  Each storage array has 32 front-end ports, which could support maximum of 16 servers
  Each storage array has the disk capacity to support a maximum of 32 servers

## Slide 45: Exercise: FC SAN (contd..)
Organization’s challenges/requirements
  Organization needs to deploy additional 45 servers to meet growth requirements
  Existing storage arrays are poorly utilized and adding of new servers require to purchase new arrays
  Organization wants to implement FC SAN to overcome the scalability and utilization challenges
  Hop count must be minimized to meet performance requirement
Task
  Propose a FC switched fabric topology to address organization’s challenges/requirements and justify your choice
  If 72-port FC switches are available, determine the minimum number of switches required in the fabric