## Slide 1: Module – 6 Internet Protocol san and fibre channel over ethernet
Module 6: IP SAN and FCoE
1
Notes: Module – 6
IP SAN and FCoE

## Slide 2
Upon completion of this module, you should be able to:
  Describe IP SAN protocols, components, and topology
  Describe FCoE protocol, components, and topology
Module 6: IP SAN and FCoE

## Slide 3: Module 6: IP SAN and FCoE
During this lesson the following topics are covered:
  Drivers for IP SAN
  IP SAN Protocols: iSCSI and FCIP
  Components, topologies, and protocol stack for iSCSI and FCIP
Lesson 1: IP SAN

## Slide 4: Drivers for IP SAN
IP SAN transports block-level data over IP network
IP is being positioned as a storage networking option because:
  Existing network infrastructure can be leveraged
  Reduced cost compared to investing in new FC SAN hardware and software
  Many long-distance disaster recovery solutions already leverage IP-based network
  Many robust and mature security options are available for IP network

## Slide 5: IP SAN Protocol: Internet Small Computer System Interface (iSCSI)
IP based protocol that is used to connect host and storage
Encapsulates SCSI commands and data into an IP packet and transports them using TCP/IP

## Slide 6: Components of iSCSI
iSCSI initiator
  Example: iSCSI host bus adapter (HBA)
iSCSI target
  Storage array with iSCSI port
  iSCSI gateway – enables communication with FC storage array
IP network
iSCSI Port
FC Port
iSCSI Gateway
Storage Array
Server
iSCSI HBA
Storage Array
IP

## Slide 7: iSCSI Host Connectivity Options
Standard NIC with software iSCSI initiator
  NIC provides network interface
  Software initiator provides iSCSI functionality
  Requires host CPU cycles for iSCSI and TCP/IP processing
TCP Offload Engine (TOE) NIC with software iSCSI initiator
  Moves TCP processing load off the host CPU onto the NIC card
  Software initiator provides iSCSI functionality
  Requires host CPU cycles for iSCSI processing
iSCSI HBA
  Offloads both iSCSI and TCP/IP processing from host CPU
  Simplest option for boot from SAN

## Slide 8: iSCSI Topologies: Native iSCSI
iSCSI initiators are either directly attached to storage array or connected through IP network
  No FC component
  Storage array has iSCSI port
Each iSCSI port is configured with an IP address
Storage Array
iSCSI Port
Server
iSCSI HBA
IP

## Slide 9: iSCSI Topologies: Bridged iSCSI
iSCSI gateway is used to enable communication between iSCSI host and FC storage
iSCSI gateway works as bridge between FC and IP network
  Converts IP packets to FC frames and vice versa
iSCSI initiator is configured with gateway’s IP address as its target
iSCSI gateway is configured as FC initiator to storage array
FC HBA
Server
iSCSI HBA
Storage Array
FC Port
iSCSI Gateway
Server
IP
FC SAN

## Slide 10: Combining FC and Native iSCSI Connectivity
Array provides both FC and iSCSI ports
  Enable iSCSI and FC connectivity in the same environment
  No bridge devices needed
FC HBA
Server
iSCSI HBA
Storage Array
FC Port
iSCSI Port
Server
IP
FC SAN

## Slide 11: iSCSI Protocol Stack
Ethernet
IP
TCP
iSCSI
SCSI
Data
OSI Model
iSCSI Initiator
iSCSI Target
Layer 7 Application
Layer 5 Session
Layer 4 Transport
Layer 3 Network
Layer 2 Data Link
SCSI
iSCSI
TCP
IP
Ethernet
SCSI
iSCSI
TCP
IP
Ethernet
Interconnect
Commands and Data
Login and Discovery
Windows and Segments
Packets
Frames

## Slide 12: iSCSI Discovery
For iSCSI communication, initiator must discover location and name of target on a network
iSCSI discovery takes place in two ways:
  SendTargets discovery
    Initiator is manually configured with the target’s network portal
    Initiator issues SendTargets command; target responds with required parameters
  Internet Storage Name Service (iSNS)
    Initiators and targets register themselves with iSNS server
    Initiator can query iSNS server for a list of available targets

## Slide 13: iSCSI Name
iSCSI name is a unique iSCSI identifier that is used to identify initiators and targets within an iSCSI network
Two common types of iSCSI names are:
  iqn: iSCSI Qualified Name
    iqn.2008-02.com.example:optional_string
  eui: Extended Unique Identifier
    eui.0300732A32598D26

## Slide 14: IP SAN Protocol: FCIP
IP-based protocol that is used to connect distributed FC SAN islands
Creates virtual FC links over existing IP network that is used to transport FC data between different FC SANs
Encapsulates FC frames onto IP packet
Provides disaster recovery solution

## Slide 15: FCIP Topology
FCIP Gateway
FCIP Gateway
Storage Array
Storage Array
Server
Servers
Server
Servers
IP
FC SAN
FC SAN

## Slide 16: FCIP Protocol Stack
IP
Header
TCP
Header
FCIP
Header
IP Payload
SOF
FC
Header
CRC
EOF
SCSI Data
FCIP Encapsulation
FC Frame
IP Packet
FC Frame
FC to IP Encapsulation
Physical Media
IP
TCP
FCIP
FCP (SCSI over FC)
SCSI Commands, Data, and Status
Application

## Slide 17: Module 6: IP SAN and FCoE
During this lesson the following topics are covered:
  Drivers for FCoE
  Components of FCoE network
  FCoE frame mapping
  Converged Enhanced Ethernet (CEE)
Lesson 2: Fibre Channel over Ethernet (FCoE)

## Slide 18: Drivers for FCoE
FCoE is a protocol that transports FC data over Ethernet network (Converged Enhanced Ethernet)
FCoE is being positioned as a storage networking option because:
  Enables consolidation of FC SAN traffic and Ethernet traffic onto a common Ethernet infrastructure
  Reduces the number of adapters, switch ports, and cables
  Reduces cost and eases data center management
  Reduces power and cooling cost, and floor space

## Slide 19: Data Center Infrastructure – Before Using FCoE
Storage Array
Storage Array
Server
FC
Switches
Server
Servers
Servers
FC
Switches
IP
Switches
LAN

## Slide 20: Data Center Infrastructure – After Using FCoE
Storage Array
Storage Array
Server
FCoE
Switches
Server
Servers
Servers
FC
Switches
LAN

## Slide 21: Components of an FCoE Network
Converged Network Adapter (CNA)
Cable
FCoE switch

## Slide 22: Converged Network Adapter (CNA)
Provides functionality of both – a standard NIC and an FC HBA
  Eliminates the need to deploy separate adapters and cables for FC and Ethernet communications
Contains separate modules for 10 Gigabit Ethernet, FC, and FCoE Application Specific Integrated Circuits (ASIC)s
  FCoE ASIC encapsulates FC frames into Ethernet frames

## Slide 23: Cable
Two options are available for FCoE cabling
  Copper based Twinax cable
  Standard fiber optical cable
Twinax Cable | Fiber Optical Cable
Suitable for shorter distances (up to 10 meters) | Can run over longer distances
Requires less power and are less expensive than fiber optical cable | Relatively more expensive than Twinax cables
Uses Small Form Factor Pluggable Plus (SFP+) connector | Uses Small Form Factor Pluggable Plus (SFP+) connector

## Slide 24: FCoE Switch
Provides both Ethernet and FC switch functionalities
Consists of FCF, Ethernet bridge, and set of CEE ports and FC ports (optional)
  FCF encapsulates and de-encapsulates FC frames
Forwards frames based on Ethertype
  Used to indicate which protocol is encapsulated in the payload of an Ethernet frame
FC Port
Fibre Channel Forwarder (FCF)
FC Port
FC Port
FC Port
Ethernet
Port
Ethernet
Port
Ethernet
Port
Ethernet
Port
Ethernet Bridge

## Slide 25: FCoE Frame Mapping
2 - Data Link
7 - Application
6 - Presentation
5 - Session
4 - Transport
3 - Network
1 - Physical
FC - 4
FC - 3
FC - 2
FCoE Mapping
2 - MAC
1 - Physical
FC - 0 Physical
FC - 1 Data enc/dec
FC - 2 Framing
FC - 3 Services
FC - 4 Protocol map
IEEE 802.1q
Layers
FCoE Protocol Stack
OSI Stack
FC Protocol Stack
Ethernet
FC Layers

## Slide 26: Converged Enhanced Ethernet
Provides lossless Ethernet
Lossless Ethernet requires following functionalities:
  Priority-based flow control (PFC)
  Enhanced transmission selection (ETS)
  Congestion notification (CN)
  Data center bridging exchange protocol(DCBX)

## Slide 27: Priority-Based Flow Control (PFC)
Creates eight virtual links on a single physical link
Uses PAUSE capability of Ethernet for each virtual link
  A virtual link can be paused and restarted independently
  PAUSE mechanism is based on user priorities or classes of service

## Slide 28: Enhanced Transmission Selection (ETS)
Allocates bandwidth to different traffic classes such as LAN, SAN, and Inter Process Communication (IPC)
Provides available bandwidth to other classes of traffic when a particular class of traffic does not use its allocated bandwidth

## Slide 29: Congestion Notification (CN)
Provides a mechanism for detecting congestion and notifying the source
  Enables a switch to send a signal to other ports that need to stop or slow down their transmissions
Rate limiting to avoid
packet loss
Congestion
Notification Message
FCoE
Switch
FCoE
Switch
FCoE
Switch
Storage Array
(Node B)
Host
(Node A)
Congestion

## Slide 30: Data Center Bridging Exchange Protocol (DCBX)
Enables CEE devices to convey and configure their features with other CEE devices in the network
  Allows a switch to distribute configuration values to attached adapters
Ensures consistent configuration across network

## Slide 31: Module 6: Summary
Key points covered in this module:
IP SAN protocols, their components, and topologies
FCoE protocol, its components, and topology